## Slide 1: Magnetic Resonance and Medical Imaging
Lect. 4 - 4th year /Medical Physics
Dr . Hanan Abd Ali

## Slide 2: Magnet resonance Imaging Hardware
a radiographic imaging system can be identified by its main components 1- x-ray tube, 2-high-voltage generator, 3- operating console
an MRI system be identified by its main components : 1-magnet 2-computer 3- operating console
The magnet is typically a large cylindrical device that accommodates the patient during imaging. Unlike a CT gantry, the MRI magnet does not have moving parts.

## Slide 3
The only things that move are electrons in a conductor.
The patient aperture is usually approximately 60 cm in diameter.
RF coils surround the patient in this aperture. Gradient coils, shim coils, and,
in the case of an electromagnet, primary coils all surround the RF coils to produce the required magnetic fields.
The computer required for MRI is similar to that used for CT: very fast and with high capacity. During an MRI examination, more data are collected, and the computations required are longer and more difficult than those for CT.
The MRI operating console is also similar to that used for CT in that it has the same controls for post processing and annotation of an image.
The patient undergoing MRI is moved to the isocenter of the magnet to ensure that the body part to be imaged is at that position
An MRI operating console has controls for selecting the timing parameters, the field of view, and slice thickness rather than kilovolt peak, milliampere, and exposure time

## Slide 4: An Overview of Magnetic Resonance Imaging
The hydrogen nuclei in the patient, often just referred to as protons, behave like tiny bar magnets.
Hydrogen makes up 80% of all atoms found in the human body, making hydrogen extremely useful for MRI. Because hydrogen is a single-charged spinning nucleon, the hydrogen nucleus exhibits magnetism due to its angular momentum and magnetic moment.
Before the patient is put into the B0 magnetic field, the magnetic moments of the patient’s nuclei are randomly oriented (Figure 1-3).

## Slide 6
The small arrows in Figure 1-3 represent these individual proton magnetic moments, which are also referred to as magnetic dipoles.
Under normal circumstances, these magnetic dipoles(each has a north and south magnetic pole) are randomly distributed in space.
Consequently, if the net magnetic field of a patient were measured, it would be zero because all of the individual magnetic dipole moments cancel

## Slide 8: Net Magnetization
When the patient is placed in the presence of a strong external magnetic field, some of the individual nuclear magnetic moments align with the external magnetic field (Figure 1-4).
The Cartesian coordinate axis, X, Y, and Z, is always rendered with the Z-axis as the vertical axis as shown Vector diagrams that show this coordinate system will be used to develop the physics of MRI.

## Slide 9
A vector is a quantity that has magnitude and direction.
The Z-axis in Figure 1-4 is drawn along axis of the patient. By convention in MRI, the Z-axis coincides with the axis of the static magnetic field (B0).
In superconducting MR imaging systems, the static magnetic field (B0) is usually horizontal, making the Z-axis horizontal, too.
In a permanent magnet imaging system, the Z-axis is usually vertical, as in the vector diagrams that follow.

## Slide 11
The strength of the B0 magnetic field is expressed in units called tesla (T).
A frequent MRI question is, “How many gray equal 1 tesla?”
  The answer is none. A relationship does not exist between ionizing radiation and magnetic field strength. Nothing about MRI can be measured in gray because MRI does not use ionizing radiation.
With a patient positioned in a static magnetic field, proton dipoles align with the (B0) magnetic field (see Figure 1-4). This statement is an over simplification and is not entirely true.
Only one of approximately every million dipoles becomes so aligned. However, once aligned, the patient is polarized and has a net magnetization. The patient now has a north and a south magnetic
pole.

## Slide 12: Precession
In addition to polarization, another phenomenon occurs when a patient is placed in a static magnetic field. This phenomenon can be understood by considering the gyroscope.
A gyroscope has an annulus of heavy metal attached by spokes to an axis (Figure 1-5). If the gyroscope is taken into space and spins, it only spins. However, if the gyroscope spins on Earth in the presence of a gravitational field, not only will the gyroscope spin, but it will also wobble. Physicists call this wobbling motion precession
Precession
If the net magnetization is placed in the XY plane it will rotate about the Z axis at a frequency equal to the frequency of the photon which would cause a transition between the two energy levels of the spin. This frequency is called the Larmor frequency.

## Slide 15
Precession is the interaction between the spinning mass of the gyroscope and the mass of the earth that is manifest through the gravitational B0 field.
By spinning, the gyroscope creates angular momentum, which interacts with the angular momentum of the spinning Earth and causes the precessional motion.
Early space station designs were gyroscope like saucers, spinning to produce an artificial gravity. Currently, hand and foot clips provide moorings for inhabitants of the International Space Station
The gyroscope precesses in the presence of gravity; the proton precesses in the presence of B0.

## Slide 16
Similarly, if a spinning magnetic field, such as the magnetic moment of the proton (Figure 1-7), is in the presence of a static magnetic field, it will not only spin but will also precess

## Slide 18: The Larmor Equation
The following is the fundamental equation for MRI, the Larmor equation. This equation identifies the frequency of precession.
Larmor Frequency
wo = g Bo
where wo is the frequency of precession (or resonant frequency) and γ is the gyromagnetic ratio the Larmor equation relates B0, the strength of the static magnetic field, to the precessional frequency (f) through the gyromagnetic ratio (γ),
which has a precise value characteristic of each nuclear species. Sometimes you will see the gyromagnetic ratio expressed as γ, but this version is to be used only with angular frequencies scaled as radians/seconds.

## Slide 19
is the correct version of the gyromagnetic ratio to use with frequencies scaled in Hz.
Gyromagnetic ratio is to MRI what the disintegration constant (ثابت تحلل)is to radioactive decay
Each radionuclide has its own characteristic disintegration constant; each nuclear species has its own characteristic gyromagnetic ratio
The units of the gyromagnetic ratio, scaled as described above, are megahertz per tesla.
For example, hydrogen has a gyromagnetic ratio of approximately 42 MHz/T. If B0 is 1 T, then the precessional frequency is 42 MHz.
Likewise, at 1.5 T the precessional frequency is 63 MHz. The precessional frequency is also called the Larmor frequency.

## Slide 20
..
Table 1-2 shows the principal nuclei of biological interest in MRI. Medical applications of MRI concentrate on hydrogen because of its relative
abundance and high gyromagnetic ratio.
Compared with other nuclei in the body, hydrogen is the best for producing an MR signal